## Slide 1: SOLAR STILL

## Slide 2
Schematic Diagram of a Single Basin Solar Still
Tank
Absorber
Condensate channel
Excess make-up water outlet
Distilled water outlet
Transparent cover
Condensed droplets
Insulators
Make-up water inlet
Brine depth
Vapoures

## Slide 3
The Components of Solar Distill & Their Specifications
System Components | Specifications | 
 | Material | Purpose
Water basin / tank | Cement concrete or fiberglass | Container of saline water ( brick - cement can be used for basin, tank should be insulated at the base to avoid thermal loss ).
Insulation | Polyurethane Foam ( PUF ), putty, tars, silicon sealant | To prevent heat losses ( should not become brittle, cracks may form resulting in vapour leakage ).
Transparent cover | Glass or polyethylene | To transmit solar energy ( glass is heavy, prone to mechanical damage. Polyethylene has low transmittivity and requires a special layer to make it water wettable.

## Slide 4
The Components of solar distill & their specifications
System Components | Specifications | 
 | Material | Purpose
Absorber | Black butyl rubber, black polyethylene or ink or dye | To absorb the heat ( should be able to withstand temperature up to 100°C ).
Condensate channel | Aluminium galvanized iron | To collect droplets of water
Make up water inlet | PVC pipe | To supply the saline water
Excess make-up water outlet | PVC pipe | To drain the water
Storage pot | Glass, plastic | To store distilled water

## Slide 5
DESIGN OF THE SOLAR STILL
Design of solar still is very simple. One aim of doing calculation is to find out how much distilled water we will get per day from one square metre area and how much total area is required to fulfil our requirement. Following assumptions can be taken into account:
Latent heat of water evaporation – 2260 kJ / kg ( heat required to change from water to steam phase )
Density of water - 1000 kg per m3
Efficiency of solar still – 0.30 ( 30 percent, can be different depending on the design )
Average daily solar radiation on a given location - 6 kWh / m2 – d ( data varies from one location to other and one season to other season )
Amount of distilled water required per day – 15 litres ( enough for one family of 5 people for drinking and cooking requirements.

## Slide 6
Step - 1
Find out useful solar radiation
Daily available solar radiation = 6 kWh / m2-day
Useful solar radiation ( which is actually converting radiation heat energy to distilled water )
= Daily solar radiation x solar distill efficiency
= 6 x 0.3 = 1.8 kWh / m2 –day
(converting Wh to joules, 1 Wh = 3600 joules )
= 6480 kJ / m2-day

## Slide 7
Step - 2
Litres of distilled water produced per day per square metre
Latent heat of water evaporation = 2260 kJ / kg
Number of litres of distilled water produced per square meter per day efficiency of the system )
= Useful Solar Radiation
Latent Heat of Water Evaporation
= 6480 / 2260
= 2.86 litres / m2-day

## Slide 8
Step - 3
Total area of the solar distill to fulfil the requirement
Total distilled water requirement per day = 15 litres / day
Total area of the solar distill to fulfil family requirement
= Total daily requirement
Number of litres produced / day / square metre
= 15 / 2.86
= 5.23 m2

## Slide 9
Alternatively the total solar distill area required to fulfil daily requirement can be calculated using following formula
A = Q x 2.26 / G x E
Where
A - total distill area required
Q - total distilled water required per day
G - daily solar radiation in MJ / m2-day
E - efficiency of solar distill in decimal

## Slide 10
Solar Insulation Available :
The solar still output is a strong function of amount of solar radiation falling on a given location. For a given temperature, higher solar radiation results in higher amount of distilled water. Thus, more the solar insolation more is the output of solar still.
Wind Velocity :
Higher wind speed would cause of higher heat losses from the still, which will result in lower efficiency, meaning less distilled water. Thus, lesser the wind speed more is the output of solar still.
Ambient Air Temperature :
Increase in ambient temperature will increase the output of solar still because heat losses will decrease. Thus, more the ambient air temperature more is the output of solar still.
Factors affecting Solar still Performance

## Slide 11
Brine Depth :
As brine depth increases, the solar still productivity decreases. Thus, lesser the brine depth more is the output of solar still
Slope of the glass cover :
Lower glass cover slope increases the output but for practical reason it should be more than 10°, for much smaller angle the water droplets will fall in the basin. Thus, slope of solar still must be 20-30° with horizontal.
Glass material & angle :
The slop of the cover must be sufficient to ensure that the condensed water runs smoothly through the condensate channel without reflecting too much solar energy and without forming large droplets. The glass should be low absorption glazing.

## Slide 12
ECONOMICS OF SOLAR STILL
Payback period can be calculated using the following sample calculation for distilled water used in battery maintenance. According to the calculations shown in Section 4.6.2 a solar distil with 30 % efficiency will produce about 2.86 litres per day per square metre if the daily solar radiation is 6 kWh / m2- day.
Calculation of payback period for solar distill unit
Daily distill water production per unit area
= 2.86 litre / day
Cost of manufacturing of solar distill for one square metre area
= Rs 1500 / m2
Cost of distill water in the market
= Rs 10 / litre

## Slide 13
Worth of distill water produced everyday ( gain )
= 2.86 x 10 = Rs 28.6 / day
The number of days required to recover the cost of solar distil
= Cost of manufacturing
Cost gain per day
= 1500 / 28.6 = 52.31
= 53 days
Thus, it can be seen that the payback period for solar distill is within 2 to 3 months.